## Slide 1: Network Programmability as a Cloud Service
Deepanshu Lulla Anuj Tyagi
Akshay Battaje Amey Uchagaonkar
Mentor: Dr. Somaya Arianfar

## Slide 2: PROJECT OVERVIEW
Goals
Offer Network Programmability as a service
Solving problem of scaling across multiple IaaS providers in MOC
Users
Infrastructure as a Service (IaaS) providers
End Product
Provide APIs to IaaS providers

## Slide 3: Software defined networks(overview)
Business Applications
Network Services
SDN
Control
Software
API
API
Network Devices
Network Devices
Network Devices
Network Devices
Network Devices
Network Devices
Application
Layer
Control
Layer
Infrastructure
Layer
Control Data Plane Interface (e.g. OpenFlow)
Software Defined Networking (SDN) is an emerging network architecture where network control is decoupled from forwarding and is directly programmable.

## Slide 4: Terms and definitions
Administrative Domain
Group of networks under one IaaS provider.
Network Abstraction Layer
Separates control plane into two parts. (eg OpenVirteX, Flow visor)

## Slide 5: Proposed Project Architecture
Controller N
Switch 1
Switch 2
Controller 1
Network Abstraction layer
Host 1
Host 2
Host 3
Host 4
Administrative Domain 1
Controller N
Switch 3
Switch 4
Controller 1
Network Abstraction layer
Host 5
Host 6
Host 7
Host 8
Administrative Domain 2

## Slide 6: Sprint 1
Create a simple network topology in Mininet
Send packets across multiple OpenV Switches using Open Daylight controller

## Slide 7: Tools and Technologies: Mininet
Network emulator
  Hosts behave like real machine.
  Allows modelling of network based on bandwidth, latency etc.
Uses Python/Command line arguments(mn) to create topologies
Figure adapted from [3]

## Slide 8: Tools and Technologies: Open Flow
Open standard to control forwarding tables of network devices
Standardized protocol – control forwarding of switches across multiple vendors
Separates data plane and control plane
Figure taken from [1]

## Slide 9: Tools and Technologies: Flow table
Figure adapted from [2]

## Slide 10: Tools and Technologies: Open virtual switch
Open-source distributed virtual multilayer switch. Main components: OVS-vswitchd, OVS-database(OVSDB)-server and OVS-kernel
Decides how to process packet made in user space
In a virtual network, virtual switch acts like an advanced edge switch for VMs.

## Slide 11: Tools and Technologies: Controller
An SDN Controller in a software-defined network (SDN) is the “brains” of the network.
It is the strategic control point in the SDN network, relaying information to the switches/routers ‘below’ (via southbound APIs) and the applications and business logic ‘above’ (via northbound APIs). [4]
Adapted from [5]

## Slide 12: Tools and Technologies: Open daylight Controller
Formed in April 2013
Open source SDN project hosted by the Linux Foundation.
Created in order to advance software-defined networking (SDN) adoption and
form basis for a strong network functions virtualization (NFV).
Founding members included Arista Networks, Big Switch Networks, Brocade, Cisco, Citrix, Ericsson, HP, IBM, Juniper Networks, Microsoft, NEC, Nuage Networks, PLUMGrid, Red Hat, and VMware

## Slide 13
Service Abstraction Layer/Core
Base Network Functions
Lithium
OpenFlow Enabled Devices
DLUX
VTN Coordinator
OpenStack Neutron
SDNI Wrapper
Network Applications
Orchestrations & Services
Open vSwitches
Additional Virtual & Physical Devices
Data Plane Elements
(Virtual Switches, Physical Device Interfaces)
Controller Platform Services/Applications
OpenFlow Stats Manager
OVSDB
NETCONF
PCMM/COPS
SNBI
LISP
BGP
PCEP
SNMP
SXP
Southbound Interfaces &
Protocol Plugins
OpenFlow
OpenFlow Switch Manager
USC
CAPWAP
OPFLEX
CoAP
HTTP
OpenFlow Forwarding Rules Mgr
L2 Switch
Host Tracker
Topology Processing
AAA AuthN Filter
OpenDaylight APIs REST/RESTCONF/NETCONF
Data Store (Config & Operational)
Messaging (Notifications / RPCs)
LACP
Network Services
Service Function Chaining
Reservation
Virtual Private Network
Virtual Tenant Network Mgr.
Unified Secure Channel Mgr
OVSDB Neutron
Device Discovery, Identification & Driver Management
LISP Service
DOCSIS Abstraction
SNMP4SDN
Network Abstractions (Policy/Intent)
ALTO Protocol Manager
Network Intent Composition
Group Based Policy Service
Platform Services
Authentication, Authorization & Accounting
Neutron Northbound
Persistence
SDN Integration Aggregator
Time Series Data Repository
Link Aggregation Ctl Protocol
Notes: Lithium Diagram, July 2015

## Slide 14: Sprint 1:Creating a SDN based network
10.2
Controller
Switch 1
Host
A
Host
B
Switch 3
Host
C
Switch 2
10.0.0.1
10.0.0.3
10.0.0.2

## Slide 15: DEMO

## Slide 16
$sudo mn --controller=remote,ip=127.0.0.1 --topo=linear,3

## Slide 18: Analysis of packets
Notes: We need to show a pcap file here for analysis. Also need to add a sl

## Slide 19: SPRINT 2:goals
User Story: Create administrative domain with multiple networks
Developing a learning switch(layer 2 or 3) with OpenDaylight.
Connect the multiple networks in current topology

## Slide 20: Sprint 2:Scaling to multiple networks
Controller
Switch 1
Host
A
Host
B
Switch 3
Host
C
Switch 2
Switch 4
Host
D
Subnet 1
Subnet 2

## Slide 21: References
[1] https://s3f.iti.illinois.edu/usrman/openflow.html
[2] http://yuba.stanford.edu/cs244wiki/index.php/Overview
[3] Stanford seminars
[4] http://searchsdn.techtarget.com/definition/SDN-controller-software-defined-networking-controller

## Slide 22: QUESTIONS?